## Slide 1
Intel DevCloud Training Module
Designing AFUs w/ RTL Code
Basics + Memory-Mapped I/O using Core Cache Interface Protocol
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction
FPGA-implemented functions: Acceleration Function Units (AFUs)
These slides will demonstrate:
  How to create AFUs with RTL code
  Basic AFU requirements
  AFU communication with processor
    Using memory-mapped I/O
    FPGA can also read/write CPU memory (not covered in these slides)
Will focus on RTL issues
  OPAE software API discussed in another video
Code examples and exercises provided to expand on slides
*image from Intel Acceleration Stack Quick Start Guide for Intel® Programmable Acceleration Card with Intel® Arria® 10 GX FPGA

## Slide 3: AFU RTL Design Considerations
Designer responsibilities:
  Identify what function to accelerate
  Identify potential parallelism in function
    For FPGAs, usually “deep” pipeline parallelism for streaming data
    Pipelines take multiple cycles to produce output, but can start new inputs before previous input is finished
    Works well with data “streams,” where inputs arrive continuously
  Creating parallel circuit in a hardware-description language
    SystemVerilog, Verilog, VHDL
  Test and verify AFU functionality and performance
  Integrate AFU into software
Intel APIs, libraries, tools
  OPAE: software API for communicating with AFU from software
  ASE (AFU Simulation Environment): hardware/software co-simulation
  Quartus: RTL synthesis, placement-and-routing, timing closure

## Slide 4: AFU Top-Level Module
AFU interface provided in ccip_std_afu.sv
  Clocks
  Reset and status
  CCI-P structure for communication with host processor
module ccip_std_afu
(
// CCI-P Clocks and Resets
input logic pClk, // Primary CCI-P interface clock.
input logic pClkDiv2, // Aligned, pClk divided by 2.
input logic pClkDiv4, // Aligned, pClk divided by 4.
input logic uClk_usr, // User clock domain.
input logic uClk_usrDiv2, // Aligned, user clock divided by 2.
input logic pck_cp2af_softReset, // CCI-P ACTIVE HIGH Soft Reset
input logic [1:0] pck_cp2af_pwrState, // CCI-P AFU Power State
input logic pck_cp2af_error, // CCI-P Protocol Error Detected
// CCI-P structures
input t_if_ccip_Rx pck_cp2af_sRx, // CCI-P Rx Port
output t_if_ccip_Tx pck_af2cp_sTx // CCI-P Tx Port
);

## Slide 5: AFU Basics
AFU exists within partial reconfiguration (PR) region of FPGA
  AFU can be reconfigured separately from rest of the FPGA
PR regions are configured with a bitstream
  “Green” bitstream configures PR region with AFUs
  “Blue” bitstream configures PR region with FPGA Interface Manager
PR regions require all I/O to be registered
  Implemented by ccip_interface_reg module in ccip_std_afu.sv:
ccip_interface_reg inst_green_ccip_interface_reg
(
.pClk (pClk),
.pck_cp2af_softReset_T0 (pck_cp2af_softReset),
.pck_cp2af_pwrState_T0 (pck_cp2af_pwrState),
.pck_cp2af_error_T0 (pck_cp2af_error),
.pck_cp2af_sRx_T0 (pck_cp2af_sRx),
.pck_af2cp_sTx_T0 (pck_af2cp_sTx_T0),
…

## Slide 6: AFU Basics
afu afu
(
.clk (pClk),
.rst (pck_cp2af_softReset_T1),
.rx (pck_cp2af_sRx_T1),
.tx (pck_af2cp_sTx_T0)
);
Provided examples use simplified afu module (afu.sv)
  Instantiated within ccip_std_afu.sv
  Single clock signal, can be changed within ccip_std_afu to any clock
  Simplified interface names
    pck_cp2af_sRx => rx, pck_af2cp_sTx => tx, etc.
  All I/O already registered
module afu
(
input clk,
input rst,
// CCI-P signals
input t_if_ccip_Rx rx,
output t_if_ccip_Tx tx
);
AFU Module Definition (afu.sv)
AFU Instantiation (in ccip_std_afu.sv)

## Slide 7: Auto-Generated Headers
Both RTL code and C++ code require access to same information
  e.g. AFU name, identifier
Shared information is specified in JSON file
  Compilation, simulation, and synthesis scripts auto-generate C++ and SystemVerilog headers with constants
  Avoids coherency problems
Data Needed
by Software
and Hardware
#define AFU_ACCEL_NAME "afu"
…
`define AFU_ACCEL_NAME "afu"
…
Header Generation Scripts
afu_json_info.h
afu_json_info.vh

## Slide 8: JSON Configuration File
JSON file provides many configuration options
For tutorial example, we just need:
  Accelerator name (e.g. “afu”)
  Universally unique identifier (UUD), produced by running uuidgen from command line
{
"version": 1,
"afu-image": {
"power": 0,
"afu-top-interface":
{
"class": "ccip_std_afu"
},
"accelerator-clusters":
[
{
"name": "afu",
"total-contexts": 1,
"accelerator-type-uuid": "c8c59ff8-a22c-49f1-851f-a04c1217c7ee"
}
]
}
}

## Slide 9: CCI-P: Core Cache Interface Protocol
Enables communication between CPU and FPGA/AFU
  Memory mapped I/O (MMIO)
    Allows CPU to access FPGA resources
    All requests initiated by CPU, FPGA responds to requests
    Transfers one 32-bit or 64-word
    Transfers cannot overlap
  FPGA access to host-processor memory (not explained in these slides)
    FPGA-initiated requests to main memory of host processor
    Transfers arbitrary number of cache lines
    Transfers can overlap
Tradeoffs
  MMIO: simple to use, low throughput
    Useful for control or non-streaming inputs
  Host-processor memory: difficult to use, high throughput
    Useful for streaming data from memory, or accessing large arrays

## Slide 10: CCI-P: Core Cache Interface Protocol
Basic structure:
  One receive (Rx) port, and one transmit (Tx) port (from point of view of FPGA)
  Several channels within each port (c0 to c2)

## Slide 11: CCI-P: MMIO Write
MMIO write transfers data from CPU into the FPGA
  Only uses CCI-P receive (Rx) channel 0
Assertion of c0.mmioWrValid specifies CPU is writing data to FPGA
  Corresponding address and write data provided in the same cycle
CCI-P provides no acknowledgement system for MMIO writes
  AFU must store write data somewhere in the cycle that it appears
  New write data can potentially show up every cycle
*c0.hdr.address doesn’t directly exist in the interface
  c0.hdr is overloaded for different uses, explained in next slide
Provided addresses are 32-bit word addresses

## Slide 12: CCI-P: MMIO Write
logic [63:0] user_reg;
// Get the header for an MMIO request
t_ccip_c0_ReqMmioHdr mmio_hdr;
assign mmio_hdr = t_ccip_c0_ReqMmioHdr'(rx.c0.hdr);
// Write to a register when the MMIO write valid is asserted
// and the MMIO header address matches the register’s address
always_ff @(posedge clk)
begin
if (rx.c0.mmioWrValid == 1)
begin
case (mmio_hdr.address)
16'h0020: user_reg <= rx.c0.data[63:0];
endcase
end
end
Example: write to 64-bit register user_reg mapped to addr 0x0020
  Note: reset code omitted on slide but included in provided afu.sv code

## Slide 13: CCI-P: MMIO Write
user_reg
=
mmio_hdr.address
0x0020
rx.c0.mmioWrValid
en
clk
rx.c0.data
Suggestion: understand synthesized circuit
  Non-blocking assignment on rising edge of clk creates register
  Case statement creates an equals comparator for each case
  Register enabled when MMIO write address matches register address and when rx.c0.mmioWrValid is asserted
  Note: may synthesize differently depending on the FPGA lookup tables

## Slide 14: CCI-P: MMIO Read
Read request from software specified by assertion of c0.mmioRdValid
Corresponding address and transaction ID (tid) provided during same cycle
FPGA responds by asserting c2.mmioRdValid when the corresponding read data is available
In same cycle, FPGA provides transaction ID to specify which read request is being responded to (in case of multiple pending requests), along with read data
*c0.hdr.address and c0.hdr.tid don’t directly exist in the interface
  c0.hdr is overloaded for different uses, will explain in later slides

## Slide 15: CCI-P: MMIO Read
In most use cases, FPGA provides read data one cycle after request
  Possible because MMIO generally accesses registers and RAMs
Figure illustrates this common use case
  Allows for simpler implementation of MMIO
  No need to save transaction IDs because the response is always one cycle later
Reads can be responded to out of order
  But, requires buffering of transaction IDs
  In most cases, best to use method illustrated here

## Slide 16: CCI-P: MMIO Read
always_ff @(posedge clk or posedge rst)
begin
if (rst) begin
.... // Reset code omitted on slide, see code example
end
else begin
// Clear read response flag every cycle
tx.c2.mmioRdValid <= 0;
// Check for MMIO read request
if (rx.c0.mmioRdValid == 1'b1) begin
// Respond with the TID of the request, and specify the data is valid
tx.c2.hdr.tid <= mmio_hdr.tid;
tx.c2.mmioRdValid <= 1;
// Provide the data
case (mmio_hdr.address)
16'h0020: tx.c2.data <= user_reg;
default: tx.c2.data <= 64'h0; // Return 0 for invalid addresses
endcase
Example: read from 64-bit register user_reg mapped to addr 0x0020

## Slide 17: CCI-P: MMIO Read
user_reg
=
mmio_hdr.address
0x0020
rx.c0.mmioRdValid
en
Synthesized circuit
  Non-blocking assignments on rising edge of clk creates registers
  Registers conveniently delay TID and mmioRdValid by a cycle
  Encoder selects mux input to store in tx.c2.data register based on MMIO address
  Combine with MMIO write code to define input to user_reg
tx.c2.data
Encoder
….
….
….
tx.c2.hdr.tid
mmio_hdr.tid
tx.c2.mmioRdValid
= register (clk not shown)

## Slide 18: CCI-P: MMIO Read
AFUs require several MMIO addresses to return specific information
  AFU ID must be generated with uuidgen and specified in AFU’s JSON file
  OPAE afu_json_mgr script extracts UUID from JSON file into afu_json_info.vh
  After afu_json_info.vh is generated, can directly use constants in header file
    e.g. logic [127:0] afu_id = `AFU_ACCEL_UUID;
case (mmio_hdr.address)
// AFU header
16'h0000: tx.c2.data <= {
4'b0001, // Feature type = AFU
8'b0, // reserved
4'b0, // afu minor revision = 0
7'b0, // reserved
1'b1, // end of DFH list = 1
24'b0, // next DFH offset = 0
4'b0, // afu major revision = 0
12'b0 // feature ID = 0 };
// AFU_ID_L
16'h0002: tx.c2.data <= afu_id[63:0];
// AFU_ID_H
16'h0004: tx.c2.data <= afu_id[127:64];
// DFH_RSVD0 and DFH_RSVD1
16'h0006: tx.c2.data <= 64'h0;
16'h0008: tx.c2.data <= 64'h0;