## Slide 1
Intel DevCloud Training Module
Intel Platform Acceleration Card (PAC) Overview
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction: Heterogeneous Computing
µP
FPGA/
GPU
int main() {
…
slow_func();
…
}
General-purpose microprocessors are flexible
  But, can be slow for some types of computation
Heterogeneous computing
  Partition app across different computing resources
  Use “accelerators” for intensive functions
    Often provide much higher parallelism than microprocessor
    Microprocessor handles less intensive parts
  Examples:
    Microprocessor + GPU
    Microprocessor + FPGA (field-programmable gate array)

## Slide 3: Intel Platform Acceleration Card (PAC)
PCI Express (PCIe) accelerator card
  Uses Arria 10, Stratix 10 field-programmable gate array (FPGA)
FPGAs implement custom hardware to accelerate software
  Especially effective for energy-efficient acceleration
PAC provides FPGA with on-board DDR4 RAM
  Can also access host processor’s main memory
  Provides networking interface for low-latency networking
*images from https://www.intel.com/content/www/us/en/programmable/products/boards_and_kits/dev-kits/altera/acceleration-card-arria-10-gx/overview.html

## Slide 4: PAC Applications
Where is PAC used?
  Networking
    Security, monitoring, function virtualization
  Streaming analytics
  Financial technology (Fintech)
    Banking, investment, risk management
  Genomic sequencing
  Video transcoding, media processing
  Machine learning
  Anything with significant parallelism
See Intel FPGA Acceleration Hub for detailed examples
  https://www.intel.com/content/www/us/en/programmable/solutions/acceleration-hub/solutions.html

## Slide 5: FPGAs vs GPUs
How do FPGAs and Intel PAC compare to GPUs?
  Highly application dependent
  GPUs have higher peak computational throughput
    But, not always possible to achieve peak throughput
  FPGAs are generally lower power
    10s of Watts vs. 100-200 Watts
  FPGAs can be more energy efficient
    Large-scale systems: data centers and supercomputers
      Power and cooling costs millions of dollars per year
    Embedded systems
      FPGA system-on-a-chip (SoC) provides low “SWaP”
      Size, weight, and power
  FPGAs are much more difficult to program in most cases

## Slide 6: Acceleration Functional Units (AFUs)
Intel refers to custom hardware in FPGA as “AFU”
Common PAC application:
  Software on host processor
  AFU running on PAC’s FPGA
Host processor uses OPAE API for FPGA communication
  Open Programmable Acceleration Engine
FPGA Interface Manager (FIM) provides hardware interface for communication
*image from Intel Acceleration Stack Quick Start Guide for Intel® Programmable Acceleration Card with Intel® Arria® 10 GX FPGA

## Slide 7: FPGA Interface Manager (FIM)
FIM provides three interfaces for AFU
  Host processor over PCIe
    Host memory (FPGA-initiated)
    Memory-mapped I/O (SW initiated)
    Uses CCI-P
    Core Cache Interface Protocol
  External (on-board) memory
    e.g. DDR4 RAM
  High-speed serial interface
    e.g. networking
*image from Intel Acceleration Stack Quick Start Guide for Intel® Programmable Acceleration Card with Intel® Arria® 10 GX FPGA

## Slide 8: How to Design AFUs?
Register-transfer-level (RTL) code
  Summary: Use hardware description languages to specify low-level hardware details
  Tradeoffs: High flexibility, high performance and efficiency, very difficult, low productivity
  Examples: Verilog, SystemVerilog, VHDL
High-level code
  Summary: Use higher-level descriptions that abstract away low-level hardware
  Tradeoffs: higher productivity, less flexible specification, possibly lower performance
  Examples:
    OpenCL: language for writing parallel code on heterogeneous platforms
    DPC++: data-parallel C++ that can be compiled to different accelerators
Accelerator-specialized libraries
  Summary: call pre-implemented functions that can run on multiple accelerators
  Tradeoffs: highly optimized, easy to use, only beneficial if appropriate functions exist
  Examples:
    OneAPI: provides libraries that can run on different accelerators
    OpenVINO: Machine-learning-specialized toolkit for emulating human vision using convolutional neural nets (CNNs)

## Slide 9: Intel DevCloud
Follow-up presentations will demonstrate how to develop PAC applications using Intel DevCloud
  Development cloud of Intel hardware
DevCloud provides:
  Development nodes with FPGA tools for designing AFUs
  PAC nodes for testing and evaluating AFU performance
Training modules will demonstrate AFU design for different design-entry methods
  Can also be done on local resources