## Slide 1
Intel DevCloud Training Module
FPGA Timing Optimization
Multicycle Paths
Greg Stitt
Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Multicycle Paths
in0_r
in1_r
out0_r
32-bit Add
32
32
in2_r
in3_r
64-bit Add
64
64
32
out1_r
64
Consider simple pipeline with adders of two widths
  64-bit adder will be critical path
  How to optimize?
What if in2 and in3 only arrive every two cycles at best?
  Solution 1: use a ½ frequency clock for the 64-bit add paths
    Not ideal for small sub-circuits
    Extra overhead if input arrival rate is not constant
  Solution 2: use multicycle paths
    Tell synthesis to allow 2 cycles for 64-bit add
= FF or register
Allow 2 cycles for this path
in0
in1
in2
in3
out0
out1

## Slide 3: Setup and Hold Edges
Review:
  Setup time: time before a FF’s edge that data must arrive by
  Hold time: amount of time after an edge that FF must be stable
    Alternatively, the amount of time that must pass before the FF input changes
    Basically defines the minimum delay between FFs
But, to what edge does the setup and hold apply?
  Setup edge: the clock edge which the data must arrive before
    Actual deadline is the setup edge - setup time (ignoring skew)
  Hold edge: the clock edge which new data must arrive after
    Actual threshold is hold edge + hold time (ignoring skew)

## Slide 4: Single-Cycle Paths
Synthesis tools assume all register pairs are single-cycle paths
Setup edge is the rising edge of the destination clock, 1 cycle after the source clock
Hold edge is the rising edge of the destination clock, the same cycle as the source clock
Source Clock
Dest Clock
Setup Edge
Hold Edge

## Slide 5: Multicycle Paths
Need to tell the synthesis tool the setup edge
  Provided by multicycle path constraint
set_multicycle_path -from {source} -to {dest} -setup 2
  Specifies that the setup check should be done relative to rising edge 2
  Essentially moves the setup edge over by 1 cycle
  But, also moves the hold edge over by 1 cycle
Source Clock
Dest Clock
Setup Edge
Hold Edge

## Slide 6: Why does the hold edge move?
For synthesis, an N-cycle path means that the destination register is loaded every N cycles
  Alternatively, the destination register holds its output for N cycles
  If data arrives before cycle N-1, the register will be incorrectly overwritten
Example: 5-cycle path
  If data arrives in cycles 1-3, it will overwrite the contents of the register
  Cycle 4 is the only cycle data can arrive to preserve register for 5 cycles
Same thing applies to single-cycle paths
  Data arriving too early within same cycle overwrites destination FF
Synthesis must guarantee the hold timing (w/ buffers, delays)
  Generally not what you want (greatly slows down FPGA clocks)

## Slide 7: Changing the Hold Edge
How can we design our circuit so the hold edge does not have to move?
Solution: make destination register immune to data arriving early with delayed enable
  Enable asserted at most every N cycles
  Hold edge no longer matters, early data will be ignored
Tell synthesis about the new hold edge:
  set_multicycle_path -from {source} -to {dest} -hold 1
  Specified as negative offset from the setup edge
    For setup of N, usually want hold of N-1
  e.g.:
    set_multicycle_path -from {source} -to {dest} -setup 5
    set_multicycle_path -from {source} -to {dest} -hold 4
Source Reg
Multicycle Logic
enable
Dest Reg
….
N FFs
= FF or register

## Slide 8: Complete Design
in0_r
in1_r
32-bit Add
en0_r
en1_r
32
32
in2_r
in3_r
64-bit Add
64
64
enable
out1_r
64
out0_r
32
Constraints:
  set_multicycle_path -from {in2_r*} -to {out1_r*} -setup 2
  set_multicycle_path -from {in3_r*} -to {out1_r*} -setup 2
  set_multicycle_path -from {in2_r*} -to {out1_r*} -hold 1
  set_multicycle_path -from {in3_r*} -to {out1_r*} -hold 1
= FF or register
Source Clock
Dest Clock
Setup Edge
Hold Edge
MAX10 FPGA experiment shows improvement from 167.7 MHz to 242.4 MHz

## Slide 9: Synthesis Constraints

## Slide 10: Summary
Timing optimization involves iterative optimization of cell/logic and interconnect delays
Logic optimizations
  Reduce logic inputs
  Pipelining, retiming
  Many device-specific optimizations
Interconnect optimizations
  Minimize resources and fanout
  Pipelined interconnect
  NoC, time-multiplexing
Next presentation will demonstrate simple code example

## Slide 11: Original Circuit
in0_r
in1_r
out0_r
32-bit Add
32
32
in2_r
in3_r
64-bit Add
64
64
32
out1_r
64
Simple pipeline with adders of two widths
  64-bit adder will be critical path
What if in2 and in3 only arrive every two cycles?
  Solution 1: use a separate clock domain that runs at ½ the frequency
    Not ideal
  Solution 2: use multicycle paths
= FF or register

## Slide 12: Multicycle Path Optimization
in0_r
in1_r
add_r
32-bit Add
en0_r
en1_r
32
32
in2_r
in3_r
64-bit Add
64
64
enable
32
out1_r
64
out0_r
32
Strategy: allow the timing bottleneck to take multiple cycles
  64-bit add now has 2 cycles to complete
Enable asserted every 2 cycles
  Loads inputs to all input registers
Extra register on the 32-bit add to align out0 and out1
Two FFs enable out1 after 2 cycles
Can be extended to any # of cycles
= FF or register

## Slide 13: Multicycle Path Optimization
in0_r
in1_r
add_r
32-bit Add
32
32
in2_r
in3_r
64-bit Add
64
64
32
out1_r
64
out0_r
32
= FF or register
Allow 2 cycles for this path
Extra register to align outputs

## Slide 14: Synthesis Constraints
Previous design will work in simulation, but has synthesis problems
Synthesis assumes all paths between register should take 1 cycle
Need to inform synthesis about multicycle paths using constraints:
  set_multicycle_path -from {in2_r*} -to {out1_r*} -setup 2
  set_multicycle_path -from {in3_r*} -to {out1_r*} -setup 2
  set_multicycle_path -from {in2_r*} -to {out1_r*} -hold 1
  set_multicycle_path -from {in3_r*} -to {out1_r*} -hold 1
What do these constraints mean?

## Slide 15: Complete Design
in0_r
in1_r
add_r
32-bit Add
en0_r
en1_r
32
32
in2_r
in3_r
64-bit Add
64
64
enable
32
out1_r
64
out0_r
32
Constraints:
  set_multicycle_path -from {in2_r*} -to {out1_r*} -setup 2
  set_multicycle_path -from {in3_r*} -to {out1_r*} -setup 2
  set_multicycle_path -from {in2_r*} -to {out1_r*} -hold 1
  set_multicycle_path -from {in3_r*} -to {out1_r*} -hold 1
= FF or register
Source Clock
Dest Clock
Setup Edge
Hold Edge