## Slide 1
Intel DevCloud Training Module
FPGA Timing Optimization
Timer Optimization Example
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction
Continue with timing optimization in Quartus
  Using timer example:
    https://github.com/ARC-Lab-UF/intel-training-modules/tree/master/timing/examples/timer
Module Interface
  Inputs:
    go: starts timer
    cycles: the number of cycles to count
  Output:
    done: asserted after cycles cycles elapse
  Parameters:
    WIDTH: the number of bits in the cycles input
module timer #(parameter int WIDTH=32)
(
input clk,
input rst,
input go,
input [WIDTH-1:0] cycles,
output logic done
);

## Slide 3: Timer Functionality
Circuit waits in IDLE state until go is asserted
  When user asserts go, timer moves to WORKING state
WORKING state counts once per cycle up to cycles
When count == cycles, timer asserts done and returns to IDLE state
Actual circuit stores cycles in internal register when go is asserted
  Note: code uses count_r name to specify register status of count
IDLE:
done = 1
count == cycles / done = 1
WORKING
go == 1 / count = 1
count++ / done = 0
go == 0

## Slide 4: Timing Bottleneck
Simplified structure of provided code:
count
=
+
1
1
cycles_r
cycles
state
= register

## Slide 5: Timing Bottleneck
Simplified structure of provided code:
Timing bottleneck: wide comparator
  2*WIDTH inputs creates logic delay of 3 LUTs for width = 32
count
=
+
1
1
cycles_r
cycles
Comparator has 2*WIDTH inputs
Creates deep LUT hierarchy
state
= register

## Slide 6: Timing Optimization
count
=
+
1
1
cycles_r
cycles
Comparator now only has WIDTH inputs
Constants aren’t counted in logic inputs
Reduces logic delay
Solution: count from cycles down to 1 instead of 1 to cycles
  Reduces comparator inputs from 2*WIDTH to WIDTH bits
    Reduce logic delay
  Increases mux inputs, but mux not on critical path
    Steals slack from non-critical path
state
= register