## Slide 1
Intel DevCloud Training Module
FPGA Timing Optimization
Background and Challenges
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction
Designers specify timing constraints related to circuit
  e.g., desired clock frequency
Synthesis tools verify if designs meet all timing constraints
  Uses static timing analysis (STA)
If constraints not met, designer performs timing optimization/closure
  A design “meets timing” or “closes timing” when all constraints met
  Challenging problem
These slides explain background and underlying challenges
Follow up slides will explain how to optimize timing
Examples and exercises included on Github repo
  https://github.com/ARC-Lab-UF/intel-training-modules/tree/master/timing

## Slide 3: How to Determine Timing Constraints?
Designer specifies timing constraints based on use case:
  FPGA board provides fixed clock frequency
    Constraint: achieved clock must match or exceed the board’s frequency
  Design has real-time requirements
    e.g., a signal-processing circuit produces outputs every 1,000 cycles for 44.1 kHz audio
    Constraint: achieved clock must be 44.1 MHz
  Design has bandwidth requirements
    e.g., using a 32-bit (4-byte) bus, a circuit requires 1.6 GB/s of input bandwidth
    Constraint: achieved clock must be 1.6 GB/s / 4 bytes = 400 MHz
  Maximize performance
    Pick an aggressive constraint, optimize until met, repeat until can’t improve further
    Or, pick super-aggressive constraint and use clock reported by timing analyzer
  Many others

## Slide 4: Clock Frequency
Requirement: data must arrive at each FF before next cycle
  Clock period (Tclk) is a deadline (Tdeadline) for delay between FFs (TFF-to-FF)
  TFF-to-FF Tdeadline where Tdeadline = Tclk
  Simplified definition for ease of explanation
    Subsequent slides will gradually add real complexities
FF1
FF3
1 ns
FF2
3 ns
1 ns
5 ns = TFF-to-FF
  TFF-to-FF = 5 ns
  Clock Period (Tclk) 5 ns
  Clock Frequency 1 / Tclk
  Clock Frequency 200 MHz

## Slide 5: FF-to-FF Delays
FF-to-FF delays (TFF-to-FF) determined by summation of:
  “Cell” delays (TC)
    Any non-interconnect resource (FFs, CLBs, LUTs, RAM, DSP, etc.)
    Note that FFs have a clk-to-Q delay: time between clock edge and appearance of output Q
  Interconnect delays (TIC)
    Connections between cells (wires, connection boxes, switch boxes, etc.)
  TC = 0.2 ns + 1.5 ns + 1.5 ns = 3.2 ns
  TIC = 1 ns + 0.8 ns + 0.6 ns = 2.4 ns
  TFF-to-FF = TC + TIC = 3.2 ns + 2.4 ns = 5.6 ns
  frequency = 1 / TFF-to-FF = 1 / 5.6 ns = 178 MHz
FFsrc
FFdst
LUT
LUT
0.2 ns (clk-to-Q)
1 ns
1.5 ns
0.8 ns
1.5 ns
0.6 ns

## Slide 6: Delays, Cont.
There are frequently multiple paths between same FFs
  Must consider the path with the maximum delay
  Interconnect delays often vary across paths due to routing differences
  TC of both paths = 0.2 + 1.5 + 1.5 = 3.2 ns
  TIC of longer bottom path = 1.1 ns + 1.2 ns + 0.6 ns = 2.9 ns
  max TFF-to-FF = 3.2 ns + 2.9 ns = 6.1 ns
  frequency = 1 / 6.1 ns = 163 MHz
FFsrc
FFdst
LUT
LUT
LUT
0.2 ns
1 ns
1.1 ns
1.5 ns
1.5 ns
0.8 ns
1.2 ns
1.5 ns
0.6 ns

## Slide 7: Maximum Clock Frequency
Max clock frequency (fmax) defined by longest delay between all FFs
  Referred to as “critical path”
Critical path delay (TCP) is 10 ns (between FF3 and FF4)
  Clock period (Tclk) must be TCP or data won’t be available yet on FF4
  fmax = 1 / TCP = 1 / 10 ns = 100 MHz
FF1
FF2
FF3
FF4
FF5
FF6
4 ns
10 ns
6 ns

## Slide 8: Setup Times
Flip-flops have a setup time (Tsetup)
  Window of time before rising clock edge where changing input causes metastable output
Data must arrive at flip-flip before setup window of next clock
  TC + TIC Tclk - Tsetup (note this is still TFF-to-FF Tdeadline with Tdeadline = Tclk - Tsetup)
  Condition must be met for all paths between all FFs
  Any path with TC + TIC Tclk - Tsetup has a setup violation
Tsetup
Maximum Possible
TC + TIC
Tclk
Tdeadline

## Slide 9: Clock Skew
Clocks are high-fanout signals
  Not possible to deliver clock to every FF at the same time
  Difference in clock arrival times between FFs known as clock skew
Clock skew affects available time before setup violation
  TC + TIC Tclk + Tskew - Tsetup (still TFF-to-FF Tdeadline with Tdeadline = Tclk + Tskew - Tsetup)
Maximum Possible
TC + TIC
Tsetup
Tskew
Positive skew increases deadline
Can help avoid setup violations
Clksrc
Clkdst
Tdeadline

## Slide 10: Setup Slack
Setup slack (Ssetup) = time between setup deadline and data arrival
  Ssetup = (Tclk + Tskew - Tsetup) - (TC + TIC) = Tdeadline - TFF-to-FF
  A path with Ssetup < 0 has a setup violation, must be optimized
  Large positive slack can help with optimizing other paths (e.g., retiming)
TC + TIC
Tsetup
Tskew
Clksrc
Clkdst
Ssetup

## Slide 11: Hold Times
FF hold time (Thold) is window of time after rising clock edge
  Input changing within hold window causes metastable FF output
New data must not arrive at flip-flip during hold window
  TC + TIC Thold + Tskew
  TFF-to-FF must exceed skew and hold times
Minimum Possible
TC + TIC
Thold
Tskew
Clksrc
Clkdst
  Positive skew increases min TC + TIC
  Counter-intuitive, but data arriving too fast at next FF is a problem

## Slide 12: Hold Slack
Hold slack (Shold) = time between data arrival and hold violation
  Shold = (TC + TIC) - (Tskew + Thold)
  A path with Shold 0 has a hold violation
  Less common than setup violations
    Usually caused by clock skew
    Skew minimized by phase-locked loops (PLLs) and clock networks
TC + TIC
Thold
Tskew
Clksrc
Clkdst
Shold

## Slide 13: Timing Optimization Preview
Focus primarily on setup violations
To avoid setup violations, ensure that:
  TC + TIC Tclk + Tskew -Tsetup
  Or, simply: TFF-to-FF Tdeadline
Tdeadline generally out of control of designer
Timing optimization focuses primarily on reducing TFF-to-FF
  Two options:
  1) Reduce cell/logic delays (TC)
  2) Reduce interconnect delays (TIC)

## Slide 14: Intel Quartus Timing Analyzer
Quartus uses different naming convention
  Data Arrival Time : time signal takes to arrive at destination FF
  Data Required Time : time when signal is required to have arrived at destination FF
Timing violations occur when Data Arrival Time > Data Required Time
Image from Intel® Quartus® Prime Pro Edition User Guide: Timing Analyzer
https://www.intel.com/content/dam/www/programmable/us/en/pdfs/literature/ug/ug-qpp-timing-analyzer.pdf

## Slide 15: Data Arrival Time
Launch Edge + Source Clock Delay + µtco + Register-to-Register Delay
  Launch Edge : time of clock edge of source register (usually 0 ns)
  Source Clock Delay : delay from clock source to clock input of source register
  µtco : clock-to-output delay (aka clk-to-Q)
    Time between clock edge and output of FF
    Ignore the µ symbol, time is usually < 1 ns
Source Clock Delay
Register-to-Register Delay
Image from Intel® Quartus® Prime Pro Edition User Guide: Timing Analyzer
https://www.intel.com/content/dam/www/programmable/us/en/pdfs/literature/ug/ug-qpp-timing-analyzer.pdf

## Slide 16: Data Required Time
Data Required Time = Latch Edge + Dest Clock Delay - µtsu
  Latch Edge : time of clock edge for dest register (usually clock period)
  Dest Clock Delay : delay from clock source to clock input of dest register
  µtsu : setup time of destination register
    Ignore the µ symbol, time is < 1 ns
Image from Intel® Quartus® Prime Pro Edition User Guide: Timing Analyzer
https://www.intel.com/content/dam/www/programmable/us/en/pdfs/literature/ug/ug-qpp-timing-analyzer.pdf

## Slide 17: Comparison of Explanations
Data Required Time similar to Tdeadline
  Both represent deadline of when signal must reach destination FF
  Tdeadline uses skew instead of Dest Clock Delay
    Tdeadline = Tclk + Tskew -Tsetup
Tskew = Dest Clock Delay – Source Clock Delay
  Timing analyzer shows delay of both clocks
Data Arrival Time = TFF-to-FF + Source Clock Delay
Main point remains the same, ensure the following are true:
  Data Arrival Time Data Required Time
  TFF-to-FF Tdeadline