## Slide 1
Intel DevCloud Training Module
FPGA Timing Optimization
Optimization Strategies
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction
Review of background material
For all paths between all FFs, must ensure:
  TC + TIC Tclk + Tskew -Tsetup
    TC: cell/logic delay, TIC: interconnect delay
    Tclk: clock period, Tskew: clock skew,Tsetup: FF setup time
  Or, simply: TFF-to-FF Tdeadline
    TFF-to-FF = TC + TIC
    Tdeadline = Tclk + Tskew -Tsetup
Prevents setup violations
  Hold violations are also a problem, but less common

## Slide 3: Introduction
Setup slack (Ssetup) = (Tclk + Tskew - Tsetup) - (TC + TIC)
  Or, Ssetup = Tdeadline - TFF-to-FF
Timing analyzer will evaluate setup slack for all paths
  If Ssetup < 0 for a path, that path must be optimized
For a given clock, only have control over TFF-to-FF
Two options for optimization:
  Reduce cell/logic delays (TC)
  Reduce interconnect delays (TIC)
These slides explain common strategies for optimizing delays
  Not exhaustive, but sufficient for many applications

## Slide 4: Timing-Optimization Methodology
Set constraints
Compile design, run timing analyzer
Identify Total Negative Slack (TNS)
  Summation of slack on all failing paths
  Estimate of how much effort will be involved for timing optimization
Sort failing paths based on negative slack
Identify bottlenecks on path with worst negative slack
  Look for both logic/cell and interconnect bottlenecks
Apply relevant timing optimizations based on bottlenecks
Repeat from 5 for next most-negative path until no more failing paths
  Occasionally restart from 2 to make sure bottlenecks haven’t changed
Note: Steps 4-5 can alternatively focus on paths that fail in many instances

## Slide 5: Cell/Logic Delays
For each failing path, identify types of cells along the path
  Examples: lookup tables (LUTs), embedded RAM (e.g., M20K), DSPs
Check device-specific suggestions for each cell type, e.g.:
  Register RAM outputs
  Avoid read-during-write in RAM
  Structure multiply-accumulates to map efficiently to DSPs
  Write code to ensure inference of specific FPGA primitive
  Usually under “Recommended HDL Coding Styles”
Most common bottleneck is LUT delays
  Combinational logic divided into hierarchy of LUTs
  Optimize longest path through that hierarchy

## Slide 6: Optimizing LUT Delays
3 total LUTs
Max TC = 2 LUTs
Goal: optimize logic to decrease max LUT hierarchy depth
  An n-input LUT can implement any n-input, 1-output logic function
    Does not matter how many gates are in that function
  Any function with > n inputs will use > 1 LUT
LUT
a5-3 = b5-3
a2-0 = b2-0
Original Circuit
Synthesized Circuit for 6-input LUTs
eq
a5
a4
a3
b5
b4
b3
LUT
a2
a1
a0
b2
b1
b0
= FF or register
6
6
1
=
1
a
b
eq
LUT

## Slide 7: Optimizing LUT Delays
Strategy 1: reduce logic inputs
Comparator example
  Try to replace some inputs with constants
  e.g., count down from input to 0 instead of 0 to input
    Count (a5-0) only ever compared with 0 vs. comparison with input
Synthesized Circuit for 6-input LUTs
1 total LUT
Max TC = 1 LUT
6
6
1
=
1
Optimized Circuit
a
eq
LUT
a5
a4
a3
a2
a1
a0
eq
0
= FF or register

## Slide 8: Optimizing LUT Delays
Strategy 2: break up longest path with extra registers (pipelining)
  Tradeoff extra cycles of latency for decreased logic delays
  Commonly used where is latency not a problem
LUT
LUT
a5-3 = b5-3
a2-0 = b2-0
eq
a5
a4
a3
b5
b4
b3
LUT
a2
a1
a0
b2
b1
b0
FF
FF
Max TC = 1 LUT
But, 2 cycles before output
= FF or register
Original Circuit
6
6
1
=
1
a
b
eq
Optimized Synthesized Circuit for 6-input LUTs

## Slide 9: Optimizing LUT Delays
Strategy 3: retiming
  Move registers (forwards or backwards) to help balance logic delays
    Move from stage with low slack to stage with high slack
  Tools apply retiming automatically, but require registers to exist
    Be aware of tool restrictions and limitations of initial states for automatic usage
= FF or register
Original Circuit
+
+
Retimed Circuit
+
+
Adds one extra register, but reduces max TC from 2 adders to 1 adder

## Slide 10: Optimizing LUT Delays
Retiming, cont.
  Automatic retiming useful when manual specification is difficult
  Comparator example pipelined automatically with extra FF on output
= FF or register
LUT
LUT
a5-3 = b5-3
a2-0 = b2-0
eq
a5
a4
a3
b5
b4
b3
LUT
a2
a1
a0
b2
b1
b0
FF
FF
6
6
1
=
1
a
b
Original Circuit
Retimed Synthesized Circuit for 6-input LUTs
eq
1
Extra FF enables automatic pipelining of comparator via retiming

## Slide 11: Optimizing LUT Delays
Strategy 4: reduce precision
  Example: use 3-bit inputs instead of 6-bit inputs
  Limitation: circuit must still work with reduced precision
  More realistic examples:
    Machine learning, signal processing often perform well with reduced precision
  A reduction in inputs doesn’t always reduce LUT amounts or maximum delay
    A 4-bit comparator still has max Tc of 2 LUTs
= FF or register
Synthesized Circuit for 6-input LUTs
1 total LUT
max TC = 1 LUT
Optimized Circuit
LUT
a2
a1
a0
b2
b1
b0
eq
Original Circuit
6
6
1
=
1
a
b
eq
3
3
1
=
1
a
b
eq

## Slide 12: Interconnect Delays
After optimizing cell delays, interconnect delays (TIC) dominate
  For highly pipelined designs, TIC is often main bottleneck
Long interconnect delays can result from any combination of:
  1) Distant resources
    Optimization: find ways to place resources closer
  2) High fanout
    Optimization: reduce fanout, add cycles, and/or steal slack from other cycles
  3) Congested routing resources
    Optimization: reduce connections, resource utilization

## Slide 13: Optimizing Distant Resources
Placement tries to minimize distance of connections between resources
Distant placements primarily result from:
  High resource utilization
  Routing congestion (see later slide)
4:1 Mux
a3
a2
a1
a0
s0
s1
Mux
a3
a2
a1
a0
s1
s0
Mux
a3
a2
a1
a0
s1
s0
X
X
X
X
X
Original Circuit
Ideal ALM Placement*
Suboptimal ALM Placement*
Input a0 placed further from mux due to other placed resources (X)
= FF
= ALM
*In this example, ALM has 6-input LUT + FF

## Slide 14: Optimizing Distant Resources
Strategy 1: reduce resource utilization
  Many application-specific strategies
  Change resource types
    e.g., use embedded RAM for long FF chains, perform multiple operations in DSPs
  Sacrifice performance (if possible) for fewer resources (time multiplexing)
Mux
a3
a2
a1
a0
s1
s0
X
X
X
X
Suboptimal ALM Placement
Mux
a3
a2
a1
s1
s0
X
X
X
X
Improved ALM Placement
X
X
a0
a0

## Slide 15: Optimizing Distant Resources
Strategy 2: add FFs to breakup long connection into multiple cycles (pipelining)
  Effective, but can be awkward to implement
  Must identify distant connections and then modify design
  Placement and routing aren’t guaranteed to produce same results
    Distant resources in one compile might be close in another compile
  Increases FF usage, may cause other bottleneck
  Especially effective on FPGAs with HyperFlex (FFs embedded into interconnect)
Source
Sink
FF
FF
Problem: distant source and sink will have long interconnect delay
Possible solution: break up delay across multiple cycles

## Slide 16: Optimizing Routing Congestion
Congestion occurs when too many signals routed in the same area of the FPGA
  High contention for tracks and switch boxes
  Congested regions must be routed around
    Creates long distances, even for close placements
Strategies:
  Minimize resources
  Use time multiplexing or Network-on-Chip (NoC)
  Pipelining interconnect may help, but can also hurt
    Don’t know what nets will require additional FFs before routing
  Optimize fanout
Congested Region
Less- Congested Region

## Slide 17: Optimizing Fanout
Strategy 1: register duplication
  Problem: difficult to place all sinks close to high-fanout source
  Solution: replicate fanout source register (FF1)
  Limitation: increases fan-out of preceding signal (FF0)
    Can potentially create new bottleneck between FF0 and duplicated FF1 (steals slack)
  Deciding amount of duplication can be tricky
    Can be automatic or manually specified per signal
FF1
FF3
FF4
FF5
FF6
FF2
FF7
FF0
High fanout from FF1 creates long distances to FF2 and FF7
FF3
FF4
FF5
FF6
FF2
FF7
FF0
Duplicated FF1 shortens longest connection
FF1
FF1
Original Circuit
Optimized Circuit

## Slide 18: Optimizing Fanout
Strategy 2: pipelined fanout trees
  Handles high fanout across multiple cycles of lower fanout
    e.g. 3 cycles of 2-fanout instead of 1 cycle of 8-fanout
  Limitations:
    Increases FF usage and latency
    Manual implementation is awkward, may require exploration
  Hierarchical proximity register chains help automate
    But place restrictions on code
FF0
FF2
FF3
FF4
FF5
FF1
FF6
Original Circuit
Optimized Circuit
FF7
FF8
FF2
FF3
FF4
FF5
FF1
FF6
FF7
FF8
FF
FF
FF
FF
FF
FF
FF0

## Slide 19: Summary
Timing optimization involves iterative optimization of cell/logic and interconnect delays
Logic optimizations
  Reduce logic inputs
  Pipelining, retiming
  Many device-specific optimizations
Interconnect optimizations
  Minimize resources and fanout
  Pipelined interconnect
  NoC, time-multiplexing
Next presentation will demonstrate simple code example