## Slide 1
Intel DevCloud Training Module
Designing AFUs for the Intel PAC w/ RTL Code
Accessing CPU Memory: DMA Hardware Abstraction Layer
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Introduction
Earlier presentation showed MMIO CPU-FPGA communication
  Low-bandwidth communication
  Examples:
    Accessing control status registers
    Configuration settings
Data inputs usually require access to host-CPU memory
  Considerably higher bandwidth
  Necessary for pipelines (most AFUs)
  Examples:
    Accessing arrays, streaming
These slides show how to access CPU memory from AFU
  See dma_loopback example in repository for detailed code
    https://github.com/ARC-Lab-UF/intel-training-modules/tree/master/RTL/examples/dma_loopback

## Slide 3: Hardware Abstraction Layer
CPU memory access using CCI-P too complicated for most users
  Convert virtual byte addresses to physical cache line addresses
  Choose between 1, 2, and 4 cache lines per request
    Must ensure requests are aligned with appropriate cache line addresses
  Reorder data as it arrives from memory
  Etc.
Simplified with a custom hardware abstraction layer (HAL)
  Completely hides CCI-P from AFU interface
  Provides common direct-memory access (DMA) interface
    Convenient way of transferring arrays
  Sacrifices some of the flexibility of CCI-P for ease of use
    Sufficient for most use cases

## Slide 4: HAL DMA Read Interface
User provides starting address on rd_addr (64-bit virtual byte address)
User provides size of transfer (# of cache lines (CLs)) on rd_size
User asserts rd_go
Data availability represented by empty = ‘0’, data shows up on rd_data
Data remains on rd_data until user asserts rd_en for one cycle
DMA asserts rd_done after user reads rd_size words

## Slide 5: HAL DMA Write Interface
User provides starting address on wr_addr (64-bit virtual byte address)
User provide size of transfer (# of cache lines (CLs)) on wr_size
User asserts wr_go
User puts data to write on wr_data, signals valid data with assertion of wr_en
User must never assert wr_en when full is asserted
DMA asserts wr_done after wr_size cache lines written to memory, usually with some delay after the last user write request

## Slide 6: HAL MMIO Write Interface
Identical to CCI-P MMIO with different signal names
Assertion of wr_en specifies processor is writing data to FPGA
Corresponding address and write data provided in the same cycle
  wr_data is 64 bits
  wr_addr corresponds to 32-bit words, must be even for 64-bit accesses
  Could potentially be translated to different addressing method
Address range restricted due to other components sharing MMIO space
  Configurable within ccip_std_afu.sv

## Slide 7: HAL MMIO Read Interface
Read request from software specified by assertion of rd_en
Address to read from specified on rd_addr during assertion of rd_en
User puts corresponding read data on rd_data exactly one cycle later
Differences from CCI-P MMIO
  Data must be provided one cycle after rd_en assertion
  Eliminates need for transaction ID
  Less flexible, but supports most AFU use cases, especially with added DMA access

## Slide 8: AFU Module with HAL
module afu
(
input clk,
input rst,
mmio_if.user mmio, // MMIO Interface
dma_if.peripheral dma // DMA Interface
);
interface dma_if #(parameter int DATA_WIDTH,
parameter int ADDR_WIDTH,
parameter int SIZE_WIDTH);
typedef logic [ADDR_WIDTH-1:0] addr_t;
typedef logic [SIZE_WIDTH:0] count_t;
logic rd_go, rd_done, rd_en, empty;
logic [DATA_WIDTH-1:0] rd_data;
addr_t rd_addr;
count_t rd_size;
logic wr_go, wr_done, wr_en, full;
logic [DATA_WIDTH-1:0] wr_data;
addr_t wr_addr;
count_t wr_size;
...
interface mmio_if #(parameter int DATA_WIDTH,
parameter int ADDR_WIDTH,
parameter int START_ADDR,
parameter int END_ADDR);
logic [DATA_WIDTH-1:0] rd_data;
logic [ADDR_WIDTH-1:0] rd_addr;
logic rd_en;
logic [DATA_WIDTH-1:0] wr_data;
logic [ADDR_WIDTH-1:0] wr_addr;
logic wr_en;
...

## Slide 9: Sample AFU Code using DMA
// Specify the starting virtual address of the DMA transfer.
// Should be aligned to a cache line, but DMA will automatically align the address.
assign dma.rd_addr = rd_addr_virtual;
assign dma.wr_addr = wr_addr_virtual;
// Specify the application-specific transfer sizes (# of cache lines).
assign dma.rd_size = rd_size;
assign dma.wr_size = wr_size;
// Start the DMA with an application-specific go signal.
assign dma.rd_go = go;
assign dma.wr_go = go;
// Read from the DMA read interface when it isn’t empty and our AFU is ready for the data.
assign dma.rd_en = !dma.empty && afu_ready;
// Write to the DMA interface when it isn’t full and our AFU has a valid output.
assign dma.wr_en = !dma.full && output_valid;
// Example AFU that is done when all writes are done.
assign done = dma.wr_done;

## Slide 10: C++ HAL API
FPGA-accessed memory must be allocated in special way
  e.g., creating a 100-element integer array
  AFU afu(AFU_ACCEL_UUID);
  volatile int *input = afu.malloc<volatile int>(100);
  “volatile” is a qualifier to ensure correctness
    Compiler isn’t aware that FPGA can change memory; volatile prevents incorrect optimizations
  Pointer can be used in software like any other pointer
    But, volatile qualifier prevents use with many functions that don’t take volatile parameters
    Potentially unsafe workaround is to allocate non-volatile data:
  int *input = afu.mallocNonvolatile<int>(100);
Provide virtual address of array to AFU using MMIO, e.g.:
  afu.write(MMIO_ARRAY_ADDR, input);
Translation to physical addresses happens on FPGA outside of AFU

## Slide 11: HAL Limitations
HAL provided as an example of abstracting away complexity
  Not intended to provide all possible functionality
Limitations of provided HAL in dma_loopback example
  DMA
    One read and write channel
    Read and write word width limited to cache line
    Doesn’t provide almost_full flag
    Only supports CPU memory, not on-board RAM
  MMIO
    Reads must be provided in a single cycle
Intel provides fuller-featured, more-complex DMAs
  https://www.intel.com/content/www/us/en/programmable/documentation/tmv1511227122034.html
  https://www.intel.com/content/www/us/en/programmable/documentation/ctb1526061110715.html

## Slide 12: Summary
CCI-P provides methods for reading and writing to CPU memory
  Very flexible
  But, too complicated for non-expert RTL designers
Presented a simplified hardware abstraction layer (HAL)
  Provides a DMA interface for transferring/streaming arrays to/from CPU memory
  Provide starting address and transfer size, then assert go
  For reads, wait until interface not empty, assert read enable to advance data
  For writes, wait until interface not full, assert write enable to provide data
HAL also abstracts MMIO interface
  Not considerably simpler than CCI-P, but portable to other platforms
Separate presentation will explain underlying CCI-P memory accesses
Will likely expand on HAL functionality in future examples