## Slide 1
Intel DevCloud Training Module
Designing AFUs for the Intel PAC w/ RTL Code
Multi-Cycle MMIO Reads
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Multi-cycle MMIO Reads
Earlier presentation demonstrated single-cycle MMIO reads
  Sufficient for most use cases
  e.g., control/status (CSR) registers
MMIO can read/write resources other than registers
  Might require multi-cycle MMIO reads
  Example: memory-mapped kernel/filter coefficients for 2D convolution
    Kernel may require too many registers, use block RAM instead
    Block RAM has at least 1-cycle of read latency, often 2 cycles when registering output
  Example: memory-mapped output from circuit
    Read latency might be non-deterministic depending on when read request is made
These slides illustrate how to handle multi-cycle reads
  See mmio_mc_read example on repository*
*https://github.com/ARC-Lab-UF/intel-training-modules/tree/master/RTL/examples/mmio_mc_read

## Slide 3: CCI-P: MMIO Read
Read request from software specified by assertion of c0.mmioRdValid
Corresponding address and transaction ID (tid) provided during same cycle
FPGA responds by asserting c2.mmioRdValid when the corresponding read data is available
In same cycle, FPGA provides transaction ID to specify which read request is being responded to (in case of multiple pending requests), along with read data
*c0.hdr.address and c0.hdr.tid don’t directly exist in the interface
  c0.hdr is overloaded for different uses, see ccip_mmio example

## Slide 4: Single-Cycle MMIO Read
=
mmio_hdr.address
CSR0_ADDR
rx.c0.mmioRdValid
enable
tx.c2.data
Encoder
….
….
….
tx.c2.hdr.tid
mmio_hdr.tid
tx.c2.mmioRdValid
= register (clk not shown)
Block RAM
CSR 0
CSR n-1
mmio_hdr.address
3-cycle read latency
(Synthetic for illustrative purposes)

## Slide 5: Multi-Cycle MMIO Read (Fixed Latency)
=
mmio_hdr.address
CSR0_ADDR
rx.c0.mmioRdValid
Encoder
….
….
….
mmio_hdr.tid
= register (clk not shown)
Block RAM
CSR 0
CSR n-1
3 cycle delay
3 cycle delay
mmio_hdr.address
3-cycle read latency
(Synthetic for illustrative purposes)
3 cycle delay
tx.c2.mmioRdValid
tx.c2.data
tx.c2.hdr.tid

## Slide 6: Multi-Cycle MMIO Read (Variable Latency)
Simple delay only works with fixed latency
Instead, write read data to a FIFO whenever ready
  Registers can write into FIFO in same cycle
  Block RAMs can write data after 1+ cycles
  Other resources can provide data whenever it is ready
MMIO read response reads TID and data from FIFO when not empty
Primary challenge: write conflicts can occur for FIFO
  e.g., a read request for a register occur 2 cycles after a read request for a 2-cycle block RAM
  Solution: must implement some form of arbitration

## Slide 7: Multi-Cycle MMIO Read (Variable Latency)
Alternate strategy:
  Buffer all incoming MMIO read requests
  Handle requests in order
    Pop read request from buffer
    Wait for data to become available
    Provide read response
Limitation:
  Slow resources could cause read-request buffer to overflow
    When read requests arrive at a faster rate than responses
  Unlikely to occur since MMIO is done over PCIe on Intel PAC

## Slide 8: Summary
Demonstrated various strategies for multi-cycle MMIO reads
  Fixed latency
  Variable latency
See code example at:
  https://github.com/ARC-Lab-UF/intel-training-modules/tree/master/RTL/examples/mmio_mc_read